## Slide 1: Lifting and Moving Materials

## Slide 2: Potential Hazards
Using forklifts unsafely
Improperly stacking materials
Failing to use proper PPE
Injuries from repetitive motions

## Slide 3: Lifting Injury Factors
Weight
Size
Shape
Obstructions
Wrong position
Wrong storage
Unsafe reaching

## Slide 4: Lifting Alone
Size up the load.
Place feet close to object, about 12 inches apart.
Bend your knees, grip securely, lift straight up with legs.
Turn your body, if needed, with your feet.
Check for clear path of travel.
Bend your knees to lower the load.

## Slide 5: Lifting As A Team
Stay close to the load.
Distribute the load equally.
Give directions while lifting and moving. Plan the job and the path of travel before lifting.
Watch out for the other lifter.
Set the load down in reverse order.

## Slide 6: Handtruck Hazards
Handles: jamming
Wheels: crushing, running off
Tongue: hitting, stepping on

## Slide 7: Handtruck Safety
Low center of gravity
Tongue under load
Load placed not to slip, shift, or fall
Height for clear view ahead
Secure load
Let truck carry
Weight on axles
Face forward
Safe speed, both handles, slow and wide turns
Proper upright storage

## Slide 8: Forklift Safety
Training and license
Seatbelts
Notify if damage or problems
Stay with the truck during overturn (sit-down type)
Step backward during lateral tipover (stand-up type)
Caution on grades, ramps
Tilt to clear road surface on grades
No raising or lowering while moving
Load within weight capacity
Speed for safe stopping

## Slide 9: Forklift Safety
Slow, sound horn where vision blocked
Clear view of travel path
No passengers without seat
Set brakes, lower forks, neutralize controls to dismount
No driving up to persons in front of fixed objects
Nobody standing on forks
Workers on platforms only directly below work area
Worker restraints on platforms
Lower platform to drive

## Slide 10: Questions?