## Slide 1: Using Personal Protective Equipment (PPE)

## Slide 2: PPE and Safety
Hazards exist in every workplace in many forms.
The best way to control a hazard is at its source.
When engineering and work practice controls are not enough, PPE can help.
Employers must perform a hazard assessment, identify and provide appropriate PPE, train employees, maintain and replace PPE, and evaluating the effectiveness of PPE.

## Slide 3: PPE and Safety
Employees must:
  Wear PPE properly
  Attend PPE training
  Care for, clean, and maintain PPE
  Inform a supervisor of the need to repair or replace PPE
Requirements for PPE appear in many OSHA standards and publications.

## Slide 4: PPE and Safety
PPE is NOT a “first line of defense” against safety and health hazards on the job!
PPE is an added safety measure when all others fail.
PPE is not a substitute for following proper safety rules on the job.

## Slide 5: Eye and face protection
Hazards include:
  Flying particles
  Molten metal
  Liquid chemicals
  Acids or caustic liquids
  Chemical gases or vapors
  Potentially infected material
  Potentially harmful light radiation

## Slide 6: Eye and Face Protection
Protective eyewear includes:
  Safety glasses
  Goggles
  Welding shields
  Laser safety goggles
  Face shields

## Slide 7: Head Protection
Employees must wear head protection if:
  Objects might fall from above and strike them on the head;
  They might bump their heads against fixed objects, such as exposed pipes or beams; or
  The possibility exists for accidental contact between workers’ heads and electrical hazards.
Hard hat classes are: Class A, Class B, and Class C.
“Bump hats” offer protection from bumps and cuts, but NOT from falling or flying objects.

## Slide 8: Head Protection
Wear the right type
Inspect before use
Check for fit
Carry nothing inside
Do not push to back of head
Never drill, paint, or label
Avoid storing in direct sunlight
Replace suspension system when needed
Replace hard hat after any impact

## Slide 9: Foot and Leg Protection
Hazards include:
  Falling or rolling objects
  Crushing or penetrating materials
  Exposure to hot substances or to corrosive or poisonous materials
  Exposure to electrical hazards
Foot and leg protection includes:
  Leggings
  Metatarsal guards
  Toe guards
  Combination foot and shin guards
  Safety shoes

## Slide 10: Hand and Arm Protection
Hazards include:
  Absorption of harmful substances through the skin
  Chemical or thermal burns
  Electrical dangers
  Bruises, abrasions, cuts, and punctures
  Fractures
  Amputations

## Slide 11: Hand and Arm Protection
PPE includes: gloves, finger guards, and arm coverings or elbow-length gloves.
Types of gloves include:
  Leather, canvas or metal mesh gloves
  Fabric and coated fabric gloves
  Chemical- and liquid-resistant gloves
  Insulating rubber gloves

## Slide 12: Body Protection
Some hazards at work may require that you shield most or all of your body. These hazards include:
  Temperature extremes
  Hot flashes from molten metals and other hot liquids
  Potential impacts from tools, machinery and materials
  Body fluids
  Hazardous chemicals

## Slide 13: Hearing Protection
Hazards include:
  Irreversible hearing loss or damage
  Physical and psychological stress
Types of PPE include:
  Single-use earplugs
  Pre-formed or molded earplugs
  Earmuffs

## Slide 14: Workplace Hazards and Female Reproductive Health
Reproductive hazards include:
  Radiation
  Some chemicals
  Certain drugs
  Cigarettes
  Some viruses
  Alcohol

## Slide 15: Workplace Hazards and Female Reproductive Health
Could cause one or more health effects
May not affect every worker or every pregnancy
May enter the body through breathing in, skin contact, or swallowing

## Slide 16: Workplace Hazards and Female Reproductive Health
Chemicals stored when not in use
Wash hands after contact
No skin contact with chemicals
Know MSDSs
Know employer’s rules and procedures
Use appropriate PPE
Prevent home contamination

## Slide 17: Questions?