## Slide 1: Using Tools and Ladders

## Slide 2: Tool Hazards
Human failure
Hazardous equipment
Pure accident

## Slide 3: Safety Every Day
Appropriate clothing that fits
Right PPE
No rings, dangling jewelry
Long hair tied back
Clean, organized work area
Proper storage after use
Right tool for job
Properly adjusted, repaired
Know fire extinguisher location, use
Fire extinguishers charged
Rags in covered metal containers
Electrical equipment off after use
No frayed cords

## Slide 4: Safety Every Day
Safe lifting techniques
Alert to possible hazards
Unsafe conditions reported

## Slide 5: Hammers
Right PPE
Right hammer
Safety goggles with striking tools
No mushroomed tools
No striking hammer faces together
Hold near end of handle
Check first for tight handle
Strike squarely

## Slide 6: Screwdrivers
Right PPE
Right screwdriver
Right size blade/bit for screw
No prying
No holding screw
Keep tip away from electrical current
Clean handles after use

## Slide 7: Wrenches
Right wrench
  Crescent/adjustable
  Open-end
  Box-end
  Combination
  Pipe
  Socket
Tight fit on nut or bolt
No extenders
Force on fixed jaw with crescent/adjustable type

## Slide 8: Pliers
Right pliers
Right PPE
No hammering

## Slide 9: Files
Right file
Secure handle
File-cleaning card to clean
No hammering or prying
Work clamped at waist height
Guide point with thumb and index finger
Push forward while pressing down, release pressure on return stroke

## Slide 10: Handsaws
Right PPE
Right handsaw
  Crosscut
  Ripsaw
  Compass/keyhole
  Coping
  Hacksaw
Check for nails, other metal
Hold material securely
Hands at safe distance from blade
No forcing blade into cut
Ease up at end of cut
Clean blades after use, before storing
Proper guards on blades

## Slide 11: Power Tools
Right clothing
Never carry by cord
Never use if damaged
Tug on plug, not cord
Cord away from heat, oil, sharp edges
Disconnect at key times
Work secured with clamps, vice
Fingers off start switch/button while carrying
Keep clean and sharp
Follow user’s manual
Good footing and balance while operating

## Slide 12: Portable Circular Saw
Cord free of blade
Guard free and retractable
No nails, other metal in stock
Solid support for stock
Max speed before starting cut
Blade deep for cut only
Saw on side after finishing

## Slide 13: Portable Drill
Proper eye protection
Remove chuck key before starting
No holding onto chuck
No forcing bit into stock
Back out to clear hole
Never hold against body

## Slide 14: Power Nailer/Nail Gun
Never point at a person
No lifting by power cord
Only nails and staples designed for the tool
Hands and body away from discharge end

## Slide 15: Powder-Actuated Tools
No flammable, explosive atmospheres
Inspect before use
No loading until use
Never loaded and unattended
Hands clear of barrel end
No pointing at anyone
No fasteners into material allowing pass-through
No fasteners into very hard or brittle material
Use alignment guide

## Slide 16: Fuel-Powered Tools
Gas/fuel stored in approved containers
Engine off and cool before refilling
Proper ventilation and/or respirators in enclosed areas

## Slide 17: Portable Ladders
Right ladder
Right length and height, load rating, and non-conductive side rails when needed
Straight/extension ladders:
  Stable, level surface
  At least 3 feet above upper landing
  Both rails in contact with supporting structure
  4:1 height-to-base ratio
  Adjustable feet to level
  Partner to hold or tie/stake at top and bottom when climbing
  Never lean beyond 12 inches
  Tools, materials in belt or clothing
  Stop at third-highest rung

## Slide 18: Portable Ladders
Stepladders:
  Solid, level surface
  Never use as straight ladder
  Fully extend and lock spreaders
  Never climb or stand on braces, top step, service tray
  Protect in doorways, high traffic areas
  Lock or barricade, mark off, or monitor in high traffic area
  Small tools and work materials in belt or clothing
Free of slipping hazards
Only for intended purpose
Not on slippery surfaces unless designed for

## Slide 19: Portable Ladders
Clear around top and bottom
No moving, shifting, extending while using
Face ladder when moving up or down
Keep 3-point contact with ladder
No objects, loads that could affect balance

## Slide 20: Questions?