## Slide 1: Emergency Coordinator (guidance document section C, page 3)
Knowledge of facility operations and wastes
Locations and capabilities of spill response equipment
  Must have the authority to mobilize personnel and resources
On site or on call 24 hours a day- backup or secondary coordinator may be required but is definitely a good idea

## Slide 2: Responsibilities:
  In the event of a fire, call the fire department or attempt to extinguish the fire
  In the event of a spill, contain the hazardous waste and clean up the waste and any contaminated surfaces, materials or soils; and
  In the event of fire, explosion, or any other incident, contact the National Response Center (call 1-800-424-8802) and the DEQ 24-hour Emergency Response Hotline (call 1-800-522-0206)

## Slide 3: Posting Emergency Information Next to the Telephone
The name and telephone number of the emergency coordinator (and backups)
Location of fire extinguishers and spill control material, and, if present, fire alarms
Telephone number of the fire department, unless the facility has a direct alarm
Telephone number of emergency response contractor
Make sure information is accurate (update when necessary)
See page C-4 for a template/example page

## Slide 4: Provide Appropriate Emergency Equipment
Unless none of the hazards posed by the facility could require a particular type of equipment
(can you prove that?)
Emergency response equipment typically includes:
Internal communication or alarm system capable of providing emergency instructions to facility personnel
A telephone, a hand-held two-way radio, a cell phone or other device capable of summoning emergency assistance
Fire-control equipment, spill-control equipment and decontamination equipment; and…

## Slide 5: Provide Appropriate Emergency Equipment Continued
Emergency response equipment typically includes:
Water at adequate volume and pressure to supply a water hose or foam-producing equipment or automatic sprinklers or water spray systems
All facility communications or alarm systems, fire protection equipment, spill-control equipment and decontamination equipment must be tested and maintained as necessary to assure its proper operation in time of emergency

## Slide 6: Making Emergency Response Arrangements
You must attempt to make arrangements with local authorities (page 6)
  fire department (maybe they already visit?)
  emergency response contractors (who can you call to help or clean up spills?)
  Police
  local hospitals
Familiarize the local authorities with the layout, waste located at you facility, and the types of injuries or illnesses that could result from fires, explosions, or releases at your facility. The information given to the authorities should include:
  the layout of the facility
  types of waste and the hazards associated with the wastes at your facility
  where personnel would be working
  entrances to the facility and possible evacuation routes and…

## Slide 7: Making Emergency Response Arrangements
These communications should be documented and maintained at your facility
They could be in the form of phone logs, certified mail receipts, or email logs
Isn’t this overkill since emergencies never happen in Oklahoma?
  Tornadoes, Winds, Flash floods, Earthquakes, Hail, Heat, Cold, Ice, Lightning, Fire
  Bubba driving the forklift into the drum storage area while texting (unforeseen emergencies)