## Slide 1: EPA’s New PFAS Drinking Water Regulation
Path to Compliance

## Slide 2: Outline
1. What is PFAS?
2. What’s the Big Fuss?
3. Final PFAS Rule
4. Monitoring Requirements
5. Treatment Options
6. Funding Sources

## Slide 3: What is PFAS?
Per- and Poly-fluoroalkyl Substances
Notes: To start, we will discuss what PFAS, or Per- and Polyfluoroalkyl Substances, is and briefly go over its history

## Slide 4: Class of synthetic chemical compounds
Nearly 15,000 individual chemicals
Organic compounds with incredibly stable bond
  Does not allow chemical to break down in “normal” amount of time
Ubiquitous in environment now.
  99% of all humans have measurable levels of PFAS in their bloodstream
Short Chain vs Long Chain
  Long chain PFAS have high bioaccumulation potential
  Short chain PFAS can be more difficult to remove
Notes: PFAS is not a single compound, but is a class of chemicals that have similar makeup and properties
Large number of individual chemicals classified as PFAS.
Stable bond that takes thousands of years to break down
Leads to buildup in environment and in people
PFAS is everywhere now, despite being first developed in 20th century
Two different main types of PFAS
Short chain and long chain
Each has own risk factors
Long chain PFAS have high bioaccumulation potential
Short chain PFAS are harder to remove
Long chain break down into short chain

## Slide 5: Where is it from?
Manufacturing Processes
Fire-fighting foam
Many products that are:
Stain resistant
Waterproof (Scotchgarde)
Nonstick (Teflon)
Food packaging
Notes: Where does PFAS come from?
Manufacturing processes in idustries such as:
aerospace
automotive
construction
electronics
PFAS is in many items we use every day.
Teflon, Scotchgarde, AFFF
Carpets

## Slide 6
PFAS Production
PFAS in Industrial Products
PFAS Use in Manufacturing
PFAS in Consumer Products
Environmental Occurrence
Consumer or Residential Exposure
Occupational Exposure
Ecological Exposure
Significant exposure potential
Less significant exposure potential
Notes: This diagram is an overview of PFAS exposure from different methods and products.
There are 4 routes of exposure
Occupational –Workplace (manufacturing/industry)
Environmental – Accumulation
Ecological – Food chain/bioaccumulation
Consumer/Residential – Products
Different people are more likely to come in contact with PFAS in different ways
Part of job
Consumer products
Contaminated food/water
The focus of the new rule is on environmental and ecological exposure

## Slide 7: History of PFAS
Late 1930s
1950s
1970s
PFAS chemistry discovered
PFAS starts being used in manufacturing and consumer products
First occupational health studies on PFAS in exposed workers
Outline health impacts and blood levels
1990s
PFAS found in blood samples from general population
Early 2000s
PFAS documented in environmental samples
2016
Lifetime drinking water health advisory issued by EPA for PFOA and PFOS
2024
PFAS NPDWR released by EPA
Movie: Dark Waters
  Tells the story of Dupont lawsuit and the history of PFAS
Notes: PFAS chemistry discovered in late 1930s and quickly spread to become ubiquitous
Health studies on PFAS were first published in 1970s, and by 1990s, general population blood samples had detectable PFAS
This has not been very long, but because of its variety of uses, has spread wide to now show up everywhere

## Slide 8: What’s the big fuss?
Chemicals that last “forever” with long-term health effects.

## Slide 9: Forever Chemicals
Specifically designed to not break down
Carbon-fluorine bond is one of the strongest chemical bonds
Present in nearly all Americans
Bioaccumulates – health effects worsen as it does
Notes: PFAS are made up of chains of carbon atoms with numerous bonds to fluorine. Whether they are long chain or short-chain, the carbon fluorine bond is known to be one of the strongest in chemistry.
This causes problems, as they are very difficult to destroy once produced.
These substances are known to bioaccumulate, meaning that they can build up inside of our bodies, worsening health effects as they do so.
PFAS are believed to be present in the blood of most Americans according to the CDC
Health effects of PFAS exposure vary

## Slide 10: Health Effects
Increases risk for cancer
Reproductive problems
High cholesterol
Can lower effectiveness of vaccines
Interferes with hormones
Notes: PFAS exposure has been linked to many health effects.
Cancer: Increased chances of Kidney, prostate, and testicular cancer.
Reproductive/developmental: Decreased fertility and increased blood pressure in pregnant women. Low birth weight, developmental delays
Cholesterol: increased lipids in blood, including higher cholesterol,
Immune suppression/vaccines
Hormones: PFAS can disrupt endocrine functions, leading to hormone interference.

## Slide 11: Occurrence in Oklahoma
Notes: -Through some of the recent UCMR5 sampling we can see that there is PFAS present in Oklahoma. As more results come in, we will have a better understanding of the impact this rule will have on our state.
View this map by using EPA’s PFAS Analytic Tools on their website. You can use this tool to identify potential PFAS sources.

## Slide 12: Final PFAS Rule
Who is required to comply with the rule and what are you required to do?
Notes: -Now we will discuss the Final NPDWR on PFAS in drinking water and what that means for utilities.

## Slide 13: Who does the PFAS rule apply to?
The PFAS rule requires all Community and Non-Transient Non-Community Public Water Systems (PWSs) to test for the presence of six different PFAS compounds in their drinking water.
This rule will impact over 1,100 PWSs across the state.
Notes: Because the health effects from PFAS are largely chronic only C and NTNC PWSs will have to sample for PFAS.
-NC don’t have to sample
-Wholesale/source systems are the only one's sampling
-Consecutive systems that use purchased water are not required to sample.

## Slide 14: Important Compliance Dates
Final Rule Published
Initial monitoring must be complete
Ongoing Compliance Monitoring
Maximum Contaminant Level Compliance starts
April 26, 2031
April 26, 2024
April 25, 2027
Start April 26, 2027
Notes: - All initial monitoring must be complete by April of 2027 we will discuss the requirements for initial monitoring a little later. This monitoring is important because it determines the ongoing compliance monitoring frequency and your systems treatment needs
Compliance monitoring will start April 1, 2027 and Monitoring violations will be issued for failure to monitor.
MCL compliance will begin in 2029 giving PWSs some time to determine if treatment is necessary. Health based MCL violations start.

## Slide 15: Monitoring Requirements
How Often and Where to sample
Notes: Now that we know a little bit about the timeline for the PFAS rule let’s get into what it will require you to do.

## Slide 16: Sample Locations
PFAS Sampling should take place at the entry point(s) to your distribution system. This is after any treatment but before the first customer.
Having a combined point of entry can reduce the number of samples you would take.
Notes: -The point of entry is after treatment but before the first customer. For SW the Treatment plant is often the first customer.
-This will be where you are already taking your other EP samples like Nitrate-nitrite, VOCs and Inorganics
Combined POEs could reduce the sampling you are required to do when you have multiple sources of water.

## Slide 17: Sampling Best Practices
Use field blanks
Wash your hands
Complete bottle labels and Chain of custody (not sample time) before collection
Flush the line to mitigate chance of cross contamination
Fill sample bottles, but do not overfill
Once sample is collected, do not open bottle again
HDPE Equipment
Stainless steel equipment
Nitrile gloves
DEQ Drinking Water PFAS Sampling SOP
State Environmental Lab Services Sampling Instructions
Notes: -Avoid wearing clothing with water or stain resistant coatings when sampling or handling samples. May of these contain fluorinated compounds. (Like GoreTex, Scotchgarde) Some good alternatives can be waxed canvas with non-fluorinated waterproofing compounds.
-These compounds really can be found everywhere but there is lots of information is available online for which products are free of any PFAS compounds.
-Make sure to follow any sampling instructions and guidance from your lab
-Deq has developed a PFAS sampling SOP that can help you avoid environmental contamination when sampling and the SELS has created sampling instructions specific to the state lab.

## Slide 18: Initial Monitoring Frequency
Initial monitoring frequency will depend on source water type and population.
Initial monitoring must be complete by April of 2027.
Systems participating In UCMR5 may have completed initial monitoring through that program.
System Type | Surface Water Systems | Groundwater Systems | Groundwater Systems
Population | All Pops | >10,000 | ≤10,000
Samples required | 4 quarterly samples 2-4 months apart | 4 quarterly samples 2-4 months apart | 2 samples within 12 months 5-7 months apart
Total samples for initial monitoring | 4 | 4 | 2
Notes: All systems besides GW ≤ 10,000 must take four consecutive quarterly samples to complete initial monitoring. Any quarterly samples must be separated by at least 2 months. Ex: Taking each sample in the 2nd month of the qt all good. Take a sample in June at the end of 2q and then in July at the beginning of 3q and they will not count.
-The results from this initial monitoring will tell the systems who needs to consider treatment before the 2029 MCL compliance deadline.

## Slide 19: Ongoing Compliance Monitoring
In 2027 ongoing compliance monitoring will begin and monitoring violations will be issued for those that fail to monitor.
The ongoing compliance monitoring frequency will be based on previous results.
The trigger level is ½ the MCL for each contaminant.
Result | Frequency of sampling
Result ≥MCL | Quarterly for RAA calculation
Results <MCL but ≥ trigger level | At least 4 quarterly samples then annual monitoring after determined reliably and consistently below the MCL
Result < trigger level | Every 3 years
Notes: Based on initial monitoring results the frequency of your ongoing compliance monitoring can change.
The trigger level also applies to the unitless Hazard Index of 1
Like many of the contaminants you test for compliance determination for MCLs is done with a running annual average.
Double check >/</= for MCL

## Slide 20: Certified Laboratories and Sampling Costs
Make sure to find a DEQ accredited lab.
There are currently 2 EPA approved methods: 537.1 and 533
Notes: Reach out to compliance with any questions.
-Stress that the specificity of certain PFAS we are looking for is the reason for high analytical costs.
There may be other labs outside the state that can process the PFAS sample as well.
EPA methods
CIC = combustion ion chromatography
HRMS = high-resolution mass spectrometry
LC-MS/MS = liquid chromatography – triple quadrupole mass spectrometry

## Slide 21: MCLs and MCLGs
Chemical | Maximum Contaminant Level Goal (MCLG) | Maximum Contaminant Level (MCL)
PFOA | 0 | 4.0 ppt
PFOS | 0 | 4.0 ppt
Maximum Contaminant Level Goal (MCLG): The level of a contaminant in drinking water below which there is no known or expected risk to health. MCLGs allow for a margin of safety and are non-enforceable public health goals. Maximum Contaminant Level (MCL): The maximum level allowed of a contaminant in water which is delivered to any user of a public water system. |  | 
Notes: - As mentioned previously MCL compliance is based on a RAA
-Significant figures matter.
For the MCLs at 4.0 anything rounding to 4.1 would be in violation so 4.03 is less than MCL but 4.07 would round up.

## Slide 22: Compliance Determination
Compliance with the MCLs will be determined by a running annual average. Each sample result will be averaged over a rolling 12-month period.
This average will be used to determine compliance with the PFAS rule.
Compliance with The MCLs will be required in 2029
Notes: In the instance you are sampling at a reduced frequency and a sample comes in that violates the MCL your schedule will be returned to standard monitoring for calculation of an RAA. Running Annual Average

## Slide 23: Public Notification (PN) and the Consumer Confidence Report (CCR)
Any detects for PFAS will be reported on CCR
Any MCL violations will require additional health effect language on CCR.
Any violations will require PN.
Tier 3 PN will be required for monitoring violations.
Tier 2 PN will be required for MCL violations
One PN can be used to satisfy multiple MCL violations
Notes: -Like other contaminants (regulated or part of the UCMR monitoring) results of sampling PFAS compounds must be reported on your consumer confidence report.
-The PN for PFAS compounds follow a framework like other contaminants. Tier 2 must be complete within 30 days and for tier 3 you have 1 year.
-Wholesale systems should inform their purchasers when there is a violation.

## Slide 24: Regionalization
Is regionalization an option?
Most treatments for PFAS are expensive $$$
It might be more cost effective to switch sources or purchase from a neighboring system
Notes: Regionalization projects with another PWS are eligible for DWSRF assistance if it is the best alternative to treatment.
Extra priority is awarded to regionalization projects with a public health risk which PFAS qualifies as.

## Slide 25: Questions? Water quality help line 405-702-8100 Email us Drinkingwater@deq.ok.gov
Notes: If you have any questions going forward, reach out to your compliance coordinator or district engineer. If you are unsure, the water quality helpline at 405-702-8100 can direct your call.