## Slide 1
Lake Thunderbird TMDLs
Public Meeting
July 23, 2013

## Slide 2
Agenda
Opening remarks
Project background
Overview of the models
TMDLs and load reductions
Recommendations & permit requirements
Informal question-answer session
Comments for the record
Project website: http://www.deq.state.ok.us/WQDnew/tmdl/thunderbird/
index.html

## Slide 3: The Clean Water Act First Adopted 1972 Clean Water Goals:
July 1, 1983
Wherever attainable, Fishable Swimmable water quality
1985
Eliminate discharge of pollutants

## Slide 4: How Do We Get There ??? Two Step Approach
Technology-Based Limits For All Point Sources
Additional Water Quality Based Controls To Meet Water Quality Standards

## Slide 5: Identifying Problem Areas
Compare Monitoring Results
To
Water Quality Standards
Set Priorities
Compile Problem Areas And Priorities In the 303d List

## Slide 6: Lake Thunderbird Impairments
Aquatic Life
High Turbidity
  Target
    < 10% exceeds 25 NTU
Low Dissolved Oxygen
  Targets
    When stratified
      5 mg/L at surface
      < 50% Lake volume below 2 mg/L
    When NOT stratified
      5 mg/L for the entire water column

## Slide 7: Lake Thunderbird Impairments
Drinking Water
High Chlorophyll a
  Target
    Average < 10ug/L

## Slide 8: The TMDL Amount Of Pollution A Waterbody Can Receive Without Violating Water Quality Standards
Point Sources
Wasteload Allocations
Nonpoint Sources
Natural Background
Load Allocations

## Slide 9
The TMDL Pie
Total Load
Allocations
Total Wasteload
Allocations
Total
Unallocated
NPS 1
NPS 2
Background
Reserve
MOS
WLA 3
WLA 2
W
L
A
1

## Slide 10
Regulated
Point
Sources

## Slide 11
Project Timeline
Monitoring (2008 – 2009)
TMDL development (2010 – )
First public meeting (May 2012)
TMDL report to EPA (Nov 2012)
Public comments
Response to comments
Finalize TMDLs

## Slide 12: Lake Thunderbird Watershed-Lake Model
Lake Thunderbird TMDL Project Informational meeting
July 23, 2013
Norman, Oklahoma
Andrew Stoddard
Dynamic Solutions, LLC
Knoxville, TN

## Slide 13: Lake Thunderbird Watershed-Lake Model
Watershed and Lake Thunderbird
Water Quality Impairments
Pollutant Sources
Watershed & Lake Model
Management Scenario “What-if?”
TMDL for Lake Thunderbird

## Slide 14: Lake Thunderbird
6,070 acre reservoir
Cleveland County
Upper Little R (256 mi2)
99,600 pop (2010)
Public water supply for Norman, Midwest City & Del City
2010 303(d) list for impairment of water supply & warm water aquatic community

## Slide 15: Lake Thunderbird Designated Uses & Impairments
Flood control, water supply, recreation, fish & wildlife propagation
Lake Thunderbird is Sensitive Water Supply
Impaired for Fish & Wildlife Propagation (high turbidity and low dissolved oxygen)
Impaired for Public Water Supply (excessive chlorophyll, algae biomass)

## Slide 16: Water Quality Targets for TMDL
< 10 percent turbidity exceeds 25 NTU
Surface layer oxygen higher than 5 mg/L
< 50% lake volume below 2 mg/L
Average chlorophyll less than 10 µg/L

## Slide 17: Pollutant Sources
Stormwater runoff
Oklahoma City
Moore
Norman
Nonpoint source runoff rural , unincorporated areas

## Slide 18: Lake Thunderbird Watershed-Lake Model
Watershed and Lake Thunderbird
Water Quality Impairments
Pollutant Sources
Watershed & Lake Model
Management Scenario “What-if?”
TMDL for Lake Thunderbird

## Slide 19: Watershed
Sediment Transport
Water Quality
Sediment Bed
Management Scenarios Flow, Loads
Water Quality Targets
EFDC
HSPF
Hydrodynamics

## Slide 20: HSPF Watershed Model
Rain/meteorology
Topography
Land uses/soils
Stream channels
Overland flow
Infiltration
Groundwater
Sub-watersheds
Flow & Pollutant loads (TN,TP,BOD,TSS)

## Slide 21: HSPF Model Calibration
Model simulation from 4/18/2008 to 4/27/2009
OCC stream data collected at 5 sites (2008-2009)
Model results compared to streamflow, TSS, water temperature, oxygen, nutrients
64 Sub-Watersheds

## Slide 22: Existing Pollutant Sources
Source (%) | Total-N | Total-P | BOD | Sediment
Moore | 25% | 28% | 31% | 21%
Norman | 40% | 38% | 39% | 41%
Oklahoma City | 32% | 31% | 28% | 35%
Overland | 3% | 3% | 2% | 3%
Source (kg/day) | Total-N | Total-P | BOD | Sediment
Tributary | 303 | 60 | 610 | 29,933
Overland | 19 | 3 | 37 | 1,553
Total | 322 | 63 | 647 | 31,486
Total-P

## Slide 23: Lake Thunderbird Conceptual Model
“Cause-effect” watershed flow, sediment, nutrient loading with lake water quality
Riverine, transition, lacustrine reservoir zones control transport and water quality
Stratified in summer; well-mixed in winter
Low summer oxygen controlled by stratification and sediment oxygen demand
Internal source of nutrients from sediment bed

## Slide 24: EFDC Lake Model
HSPF Streamflow & Loads (TN,TP,BOD,TSS)
Atm-Deposition (N,P)
Internal N,P load (bed)
Velocity, Water Level
Water Temperature
Sediment (TSS)
Detrital Organic Matter
Algae
Dissolved Oxygen
Nutrients (N,P)
1660 Cells,6 Layers

## Slide 25: Lake Model Data Sources
Bathymetry: OWRB survey in 2001
Watershed Flow & Water Quality: HSPF watershed model
Meteorology: Winds, solar radiation, air temperature, precipitation, evaporation from MESONET
Lake level & releases at dam: USACE Tulsa District
Water supply withdrawals: COMCD (Norman, Midwest City and Del City)
Lake Water Quality: OWRB monitoring of 8 sites in 2008-2009 for model calibration
Sediment Bed: OWRB surveys in 2008 for nutrients and solids

## Slide 26: Lake Model Calibration
EFDC model simulation period from 4/18/2008 through 4/27/2009
OWRB monitoring data collected at 8 sites in 2008-2009
EFDC model results compared to water level, water temperature, suspended solids, dissolved oxygen, algae chlorophyll, water clarity (secchi depth), nutrients and sediment flux

## Slide 27
Dissolved Oxygen
Surface & Bottom Site 2
Aug-2008 Storm Event

## Slide 28: Aug-2008 Storm, Anoxic Volume

## Slide 29
Algae Chlorophyll-a
Surface Site 2

## Slide 30: How Well Did the Lake Model Match Observed Data?
Model generated seasonal stratification with good match to water temperature and dissolved oxygen; Aug-2008 storm event reproduced.
Model matched seasonal trends of water temperature, dissolved oxygen, water clarity (secchi depth), nutrients and chlorophyll
Model results used to compute anoxic volume of lake as percentage
Sediment flux model accounted for internal loads of N, P

## Slide 31: Lake Thunderbird Watershed-Lake Model
Watershed and Lake Thunderbird
Water Quality Impairments
Pollutant Sources
Watershed & Lake Model
Management Scenario “What-if?”
TMDL for Lake Thunderbird

## Slide 32
Watershed
WQ
Impairments
Existing Loads
Lake
Watershed
Reduce Loads
Lake
WQ Target
Compliance
Management Scenario
“What-if” 35% of TSS and nutrient (N,P) load is removed?
Would lake attain WQ targets for turbidity, Chlorophyll & DO?
How long will it take to attain compliance with WQ targets?

## Slide 33
Meets WQ Target
< 25 NTU Turbidity
Meets WQ Target
<10 µg/L
Chlorophyll
Meets WQ Target
(a) Sfc DO > 5 mg/L
(b) <50% Lake Volume
< 2 mg/L

## Slide 34: Lake Thunderbird Watershed-Lake Model
Watershed and Lake Thunderbird
Water Quality Impairments & Targets
Pollutant Sources
Watershed & Lake Model
Management Scenario “What-if?”
TMDL for Lake Thunderbird

## Slide 35: 35% Load Reduction & TMDL
35% load reduction expected to attain compliance with water quality targets
TMDL computed from Long Term Average (LTA) load based on 35% reduction of existing loads
Pollutant flow & loads are described by log-normal distribution
Probability-based statistics of log-normal distribution of watershed loading data used to compute TMDLs

## Slide 36: Total Maximum Daily Loads (kg/day)
 | Total-N | Total-P | BOD | Sediment
Existing, 2008-2009 | 322 | 63 | 647 | 31,487
Load Removal | 35% | 35% | 0% | 35%
Long-Term Average Load | 209 | 41 | 647 | 20,466
Coeff_Var (CV) | 4.25 | 4.40 | 4.77 | 5.82
TMDL | 808 | 158 | 2,481 | 76,951

## Slide 37: Total Maximum Daily Loads (kg/day)
WQ | TMDL | LA | WLA | WLA | WLA | MOS
 |  |  | Moore | Norman | OKC | 
Total-N | 808 | 21 | 205 | 319 | 262 | Implicit
Total-P | 158 | 4 | 45 | 60 | 49 | Implicit
BOD | 2,481 | 57 | 781 | 956 | 687 | Implicit
TSS | 76,951 | 2,069 | 16,236 | 31,596 | 27,050 | Implicit

## Slide 39: Frequency Distribution, TP

## Slide 40: How were WLAs assigned?
WLA % | Moore | Norman | OKC
Total Nitrogen (TN) | 26.1% | 40.6% | 33.3%
Total Phosphorus (TP) | 28.9% | 39.0% | 32.1%
CBOD | 32.2% | 39.4% | 28.3%
Suspended Solids (TSS) | 21.7% | 42.2% | 36.1%
WLAs were assigned based on the percentage of existing loadings

## Slide 41: How were WLAs assigned?
No WLA for Midwest City and Noble
  Midwest City – 0.05% of total watershed
  Noble - 0.26% of total watershed
No reductions for unincorporated area

## Slide 42
Sediment Loading TP loading

## Slide 43: Lake Management
General Recommendations
Continue hypolimnetic oxygen injection project (COMCD)
Continue/expand shoreline re-vegetation establishment (COMCD/OWRB)
Consider establishing treatment wetlands on Little River arm above Twin Bridges

## Slide 44: What does it mean for MS4 Permits?
General Recommendations
Improve controls of sewer overflows
Implement enhanced controls for on-site wastewater systems (septic tanks)
Establish a stakeholder/citizen advisory committee

## Slide 45: What does it mean for MS4 Permits?
MS4s (Moore, Norman, OKC)
Submit an approvable TMDL compliance Plan within 24 months of EPA approval
  Identify potential significant sources
  Select a General Strategy for meeting the WLAs
  Implement enhanced or more frequent construction site inspections. Consider enhanced enforcement measures.
  Determine a schedule for achieving the WLA
  Track BMP implementation
  Implement educational programs

## Slide 46: What does it mean for MS4 Permits?
MS4s (Moore, Norman, OKC) - continued
Submit either a TMDL monitoring plan or a commitment to participate in a coordinated regional monitoring program within 24 months of EPA approval
Monitoring program shall be fully implemented within 3 years of EPA approval
Utilize the monitoring data to evaluate effectiveness of BMPs and demonstrate progress toward attaining the WLAs
If progress cannot be shown, revise the compliance plan
Annual Reporting

## Slide 47: What does it mean for Construction sites?
Stormwater Construction General Permit (OKR10)
Meet all conditions in Construction General Permit (OKR10)
Additional general requirements under this TMDL
  Comply with any additional pollutant prevention or discharge monitoring requirements established by the local MS4 municipalities.
  Submit to the DEQ all Storm Water Pollution Prevention Plans (SWP3) for sites of five acres or larger

## Slide 48: What does it mean for Construction sites?
Site-specific requirements in all authorizations issued by DEQ in the Lake Thunderbird watershed
  Vegetated buffer: 100 ft minmum for all streams (or equivalent controls)
  Sediment basins for all locations draining 5 acres or more
  Weekly site inspections
  Quicker corrective actions
  Immediate stabilization
  Soil nutrient testing before using fertilizer

## Slide 49: What does it mean for Industrial Stormwater?
Industrial Stormwater
Meet conditions in Multi-Section General Permit (OKR05)
Additional requirements under this TMDL
  Update the SWP3 for additional TSS & nutrient reduction measures within 12 months
  Monthly inspection & maintenance
  Monitoring and reporting once a month if the permit has numeric effluent limits
  Comply with any additional pollutant prevention or discharge monitoring requirements established by the local MS4 municipalities
Applies to – Asphalt Paving, Concrete Products, Sand & Gravel Mining

## Slide 50
What Happens Next ?
Comments Accepted Through August 1
Comment Responsiveness Summary
Final Report Submitted For EPA Approval
Incorporate In Water Quality Management Plan

## Slide 51
How To Provide Comments
Oral or Written Comments Accepted This Evening
By Mail:
    Dr. Karen Miles
    Water Quality Division
    Oklahoma Department of Environmental Quality
    P.O. Box 1677
    Oklahoma City, OK 73101-1677
By Email:
    Karen.Miles@deq.ok.gov
Comments Must be Received by
Thursday August 1, 2013 !
Project website: http://www.deq.state.ok.us/WQDnew/tmdl/thunderbird/index.html

## Slide 52
QUESTIONS ?

## Slide 53
COMMENTS
for the record

## Slide 54
How To Provide Comments
Oral or Written Comments Accepted This Evening
By Mail:
    Dr. Karen Miles
    Water Quality Division
    Oklahoma Department of Environmental Quality
    P.O. Box 1677
    Oklahoma City, OK 73101-1677
By Email:
    Karen.Miles@deq.ok.gov
Comments Must be Received by
Thursday August 1, 2013 !
Project website: http://www.deq.state.ok.us/WQDnew/tmdl/thunderbird/index.html

## Slide 55
Thanks For Coming
Please Drive Safely